## Slide 1: Quality-of-Service (QoS) for Virtual Networks in OpenFlow MPLS Transport Networks
Ashiq Khan*, Wolfgang Kiess, David Perez-Caparros, Joan Triay
*NTT DOCOMO, Inc., Japan
DOCOMO Communications Labs, Germany
IEEE CloudNet, Nov 11-13, 2013
San Francisco

## Slide 2: Contents
Background and Objective
QoS in MPLS: an overview
Proposal
Evaluation: prototype
Conclusions

## Slide 3: Background
OpenFlow virtualizes/slices transport networks easily
  Lacks scalability, QoS support
MPLS is scalable, has carrier-grade QoS support
  Lacks virtualization capability when it comes to QoS
Cloud/Datacenter
Cloud/Datacenter
Cloud/Datacenter
How to accommodate multiple virtual networks with QoS guarantee
MPLS transport domain
OpenFlow
OpenFlow
OpenFlow
Impractical to replace all MPLS switches in one day…. but then,

## Slide 4: Objective
MPLS can isolate multiple QoS classes
  but, multiple VNs mean isolating now within a QoS class
Voice (QoS-0)
Video (QoS-1)
4G
4G
5G
5G
MPLS switch
MPLS switch
Accommodate multiple virtual networks in MPLS domain
How can we realize this without changing MPLS implementations

## Slide 5: MPLS QoS support overview
Maximum Allocation Model (MAM)
C0
C2
C1
Maximum
Reservable
Bandwidth
a. MAM
Maximum
Reservable
Bandwidth
b. RDM
C2
+
C1
+
C0
C1
+
C0
C0
Russian doll Model (RDM)
MPLS defines two bandwidth constraint models
Strict BW isolation among classes
Unused BW are wasted
Aggregated BW to a set of classes
Complex management and preemption task
Both classes need to be addressed for multiple VN accommodation

## Slide 6: Creating multiple virtual networks …. principle
Without any special support from MPLS
  Transparent to MPLS
C0
C1
+
C0
C0
C2
C1
Maximum
Reservable
Bandwidth
C2
+
C1
+
C0
Maximum
Reservable
Bandwidth
a. MAM
b. RDM
VN-0
VN-1
C0
C0
C1
+
C0
C2
+
C1
+
C0
C2
+
C1
+
C0
C1
+
C0
Need a flexible, programmable admission control mechanism

## Slide 7: Proposed architecture
LER
LER
LSR
LSR
LSR
MPLS switching domain
Source/Destination
Source/Destination
Source/Destination
Source/Destination
Source/Destination
OpenFlow switch
OpenFlow Controller
OpenFlow Domain A
MPLS
Available BW
10
15
3
10
MPLS
Max BW
QoS
class
C0
C1
+
Info from MPLS domain
Available BW
QoS class
Max BW
C0
C1
C1
6
4
8
0
3
6
C0
7
4
VN
VN-0
VN-1
Per VN reservation state
OF Domain B
Session Establishment Request
Session data transfer
LER: Label Edge Router
LSR: Label Switching Router
VN-0
VN-1
OpenFlow (OF) as the Admission Controller to the MPLS domain
The whole process remains transparent to the MPLS domain

## Slide 8: Experiment platform prototyping
Topology
Configuration
  All hosts are virtual machines (Ubuntu 12.04, VMWare, HP blade center 520)
  MPLS switches: MPLS kernel extension* on Debian 4
  Links bandwidth: 6.3 Mbps
OpenFlow Controller
(Floodlight)
OpenFlow Switch
(Open vSwitch)
MPLS LSR
MPLS LER 3
Host A
Host C
Host B
Host D
MPLS LER 2
MPLS LER 1
*MPLS Linux Labs by Sourceforge
VN1: Host A, Host B VN2: Host C, Host D
MPLS QoS BW per QoS Virtual Network BW per VN
C0 40% VN1 20%
VN2 20%
C1 60% VN1 20%
VN2 40%
Bandwidth allocation in the MPLS domain

## Slide 9: Results MAM
Achieving isolation and appropriate admission control
(a) without OF admission control
(b) with OF admission control
Fig: Accommodation of multiple VNs in MAM model
BW
Time Session Scenario 1 Scenario 2
t1 VN1-C1 30% 20%
t2 VN2-C1 40% 60%
t3 VN1-C0 20% 20%
t4 VN2-C0 20% 20%
MPLS QoS BW per QoS Virtual Network BW per VN
C0 40% VN1 20%
VN2 20%
C1 60% VN1 20%
VN2 40%
Bandwidth allocation in the MPLS domain
Isolation achieved without any modification in the MPLS domain

## Slide 10: Results RDM -1
(a) without OF admission control
(b) with OF admission control
Fig: Accommodation of multiple VNs and consequent operations in RDM model for Scenario 1
BW
Time Session Scenario 1 Scenario 2
t1 VN1-C1 30% 20%
t2 VN2-C1 40% 60%
t3 VN1-C0 20% 20%
t4 VN2-C0 20% 20%
MPLS QoS BW per QoS Virtual Network BW per VN
C0 40% VN1 20%
VN2 20%
C1 60% VN1 20%
VN2 40%
Bandwidth allocation in the MPLS domain
Achieving isolation, appropriate admission control and preemption
Intra-VN preemption is also possible without any modification in MPLS

## Slide 11: Results RDM -2
(a) without OF admission control
(b) with OF admission control
Fig: Accommodation of multiple VNs and consequent operations in RDM model for Scenario 2
BW
Time Session Scenario 1 Scenario 2
t1 VN1-C1 30% 20%
t2 VN2-C1 40% 60%
t3 VN1-C0 20% 20%
t4 VN2-C0 20% 20%
MPLS QoS BW per QoS Virtual Network BW per VN
C0 40% VN1 20%
VN2 20%
C1 60% VN1 20%
VN2 40%
Bandwidth allocation in the MPLS domain
Achieving isolation, appropriate admission control and preemption
Intra-VN preemption is also possible without any modification in MPLS

## Slide 12: Conclusions
Summary
  Proposed method for accommodating multiple virtual networks in MPLS
  Proposed method doesn’t require any change in the MPLS domain
  Verified the proposal by elementary prototype
Future Works
  QoS in the OpenFlow domain
  Large scale experiment
  Isolation guarantee at the MPLS core

## Slide 13
Ashiq Khan
khan@nttdocomo.co.jp